## Slide 1: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1 C Basics

## Slide 2: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Examining the C Template Provided by CCS
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Step 1: Create a new C/C++ project:
a) Use the pull-down menu: File – New Project.
b) In the Project Wizard screen, select: CCS Project.
c) In the New CCS Project screen, select “Empty Project (with main.c)” and give it the name C_constructs_skeleton. Use the default settings for everything else. Click “Finish.”

## Slide 3: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Examining the C Template Provided by CCS
You will see a main.c file created with the following template code:

## Slide 4: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Examining the C Template Provided by CCS
Behind the scenes configurations:
Reset vector - starting address of program memory.
Stack pointer - ending address +1 of data memory.
No need to specify whether statements will go into program memory or data memory.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 5: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
13.1 C Basics
Program file:
main.asm → main.c
Header file:
msp430.h → #include<msp430.h>
int main (void) – indication of main program in C; followed by curly brackets.
return 0 – last statement in a C program.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 6: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
13.1 C Basics
Block comment – begins with /* and ends with */
  Anything between will be commented
  Can span multiple lines.
Line comment – begins with //
  Anything after the starting syntax to the end of the line will be treated as a comment.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 7: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
13.1 C Basics
Items that do not need to be explicitly coded:
  Reset vector definition
  Stack pointer initialization
  Specification of program memory or data memory
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 8: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1 C Basics
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 9: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.1 While() Loop in C, Using Variables

## Slide 10: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
13.1.1 While() Loops in C
Executes as long as the Boolean condition provided within its parenthesis is true.
Infinite loop:
jmp main → while(1)
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 11: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Variable Storage
The compiler will automatically decide the most efficient place to store a variable.
It has the option of storing in a register, data memory, or the stack.
The storage location can be determined by looking at the variable’s address location in the Variable Viewer.
There is no need to explicitly define the location of the storage allocation.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 12: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
OPTIMIZATION!!!
Compiler will attempt to optimize the program by default – aka the compiler recognizes code that doesn’t access the outside of the MCU and can omit it.
When wanting to observe the program operation step-by-step, optimization must be turned off.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 13: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
OPTIMIZATION!!!
Steps to turn OFF optimization:
  Use the pull-down menu to select: Project → Properties.
  In the dialog that appears, click on “Optimization” and then set the “Optimization level” to “off”.

## Slide 14: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: While() Loops in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_While_Loops
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.

## Slide 15: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: While() Loops in C
Step 3:TURN OFF OPTIMIZATION!!!
Step 4: Save and debug your program. Set a breakpoint before the int count = 0; line. Run to the breakpoint.
Step 5: Click on the “Variables” tab next to the Register Viewer tab. This will allow you to see the values of any variables you declared.

## Slide 16: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: While() Loops in C
Step 6: Now step your program and observe the behavior of the while(1) loop and the value of count incrementing each time through the loop.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 17: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.1 While() Loop in C, Using Variables
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 18: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.2 For() Loop in C

## Slide 19: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
13.1.2 For() Loops in C
Allows us to easily manage the number of times the loop will execute by using a loop variable.
Programmer specifies starting value, end value, and how to increment/decrement each time through the loop.
The loop variable can be used to perform operations on other variables or as an index for addresses.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 20: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: For() Loops in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_For_Loops
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.

## Slide 21: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: For() Loops in C
Step 3:TURN OFF OPTIMIZATION!!!
Step 4: Save and debug your program. Set a breakpoint before the int i = 0; line. Run to the breakpoint.
Step 5: Click on the “Variables” tab and observe i and count.

## Slide 22: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: For() Loops in C
Step 6: Now step your program and observe the behavior of the for() loop and the value of i and count each time through the loop.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 23: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.2 For() Loop in C
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 24: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.3 If/Else Statements in C

## Slide 25: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: If/Else Statements in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_If_Else
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 26: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: If/Else Statements in C

## Slide 27: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: If/Else Statements in C
Step 3:TURN OFF OPTIMIZATION!!!
Step 4: Save and debug your program. Set a breakpoint before the for() loop. Run to the breakpoint.
Step 5: Step your program and observe “i” and “it_is_TWO” in the Variable Viewer.

## Slide 28: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.3 If/Else Statements in C
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 29: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.4 Switch/Case Statements in C

## Slide 30: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Switch/Case Statements in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Switch_Case
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 31: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Switch/Case Statements in C

## Slide 32: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Switch/Case Statements in C
Step 3:TURN OFF OPTIMIZATION!!!
Step 4: Save and debug your program. Set a breakpoint before the for() loop. Run to the breakpoint.
Step 5: Step your program and observe “i”, “it_is_ONE”, and “it_is_TWO” in the Variable Viewer.

## Slide 33: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.4 Switch/Case Statements in C
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 34: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.5 Arithmetic Operations in C

## Slide 35: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Arithmetic operators in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Arithmetic
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.

## Slide 36: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Arithmetic operators in C
Step 3:TURN OFF OPTIMIZATION!!!
Step 4: Save and debug your program. Set a breakpoint before the while() loop. Run to the breakpoint.
Step 5: Step your program and observe the variables in the Variable Viewer.

## Slide 37: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.5 Arithmetic Operations in C
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 38: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.6 Bitwise Logic Operations in C

## Slide 39: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
13.1.6 Bitwise Logic operators in C

## Slide 40: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
13.1.6 Bitwise Logic operators in C
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
These types of instructions allow us to set, clear, or toggle bits within a variable or register.
These operations are critical to setting up the sub-systems on an MCU.
bis – bit set.
bic – bit clear.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 41: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Bitwise Logic operations in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Bitwise_Logic
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 42: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Bitwise Logic operations in C

## Slide 43: Ch. 13: Switching to the C Language
13.1 C Constructs on the MSP430
Ex: Bitwise Logic operations in C
Step 3:TURN OFF OPTIMIZATION!!!
Step 4: Save and debug your program. Set a breakpoint before the while() loop. Run to the breakpoint.
Step 5: Step your program and observe the variables in the Variable Viewer.

## Slide 44: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.1.6 Bitwise Logic Operations in C
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 45: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.2 Digital I/O in C - Outputs

## Slide 46: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
13.2 Digital I/O in C
All of the steps that had to be done in assembly to configure the I/O system still need to be done in C.
Using a port as an output:
  Configure direction as an output (PxDIR = 1).
  Disable the I/O low power mode (clear LOCKLPM5 bit in PM5CTL0)
  Write logic levels to the port (PxOUT)
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 47: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
Ex: Using a Digital Output to Drive LED1 in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Dig_IO_Outputs_n_LEDs
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.

## Slide 48: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
Ex: Using a Digital Output to Drive LED1 in C
Step 3: Save and debug your program. Set a breakpoint before the statement to set P1DIR (P1DIR |= BIT0). Run to the breakpoint.
Step 4: Run your program to the breakpoint. Step your program to observe its operation.

## Slide 49: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
Ex: Using a Digital Output to Drive LED1 in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Dig_IO_Blinky
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.

## Slide 50: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
Ex: Using a Digital Output to Drive LED1 in C
Step 3: Save, debug, and run your program. You should see LED1 blink on and off continually.

## Slide 51: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.2 Digital I/O in C - Outputs
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 52: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.2 Digital I/O in C – Inputs and Polling

## Slide 53: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
13.2 Digital I/O in C
Using a port as an input:
  Setting the port direction to an input (PxDIR = 0).
  Enabling a pull-up/down resistor (PxREN = 1).
  Setting the polarity of the resistor (PxOUT).
  Reads the input (PxIN).
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 54: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
Ex: Polling the Input S1 with Delay in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Dig_IO_Inputs_n_Polling_S1
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.

## Slide 55: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
13.2 Digital I/O in C
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
In the case of S1, we only care about bit 1.
We can clear out all other bits in the variable using a bitwise AND with 0b00000010.
Once this is done, SW1 can be used to check if the button was pressed.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 56: Ch. 13: Switching to the C Language
13.2 Digital I/O in C
Ex: Polling the Input S1 with Delay in C
Step 3: Save, debug, and run your program. You should see LED1 turn on when you press S1.

## Slide 57: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.2 Digital I/O in C – Inputs and Polling
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 58: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.3 Interrupts in C

## Slide 59: Ch. 13: Switching to the C Language
13.3 Interrupts in C
13.3 Interrupts in C
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Steps to use a maskable port interrupt:
  Configure the peripheral for the desired functionality.
  Clear the peripheral’s interrupt flag (PxIFG).
  Assert the local interrupt enable (PxIE) for the peripheral.
  Assert the global interrupt enable (GIE) in the status register.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 60: Ch. 13: Switching to the C Language
13.3 Interrupts in C
13.3 Interrupts in C
Steps to use a maskable port interrupt (cont.):
  Write ISR with an address label to mark starting location and the reti instruction to denote its end. Remember that the ISR must clear the peripherals local interrupt flag (PxIFG) so that when the ISR completes, the peripheral doesn’t inadvertently trigger another IRQ.
  Initialize the vector address for the peripheral using the ISR address label and directives.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 61: Ch. 13: Switching to the C Language
13.3 Interrupts in C
13.3 Interrupts in C
__enable_interrupt() – sets the GIE bit in the status register.
#pragma – specifies the initializing interrupt vector.
  #pragma vector = <VECTOR_LABEL>
__interrupt – denotes that the routine is an ISR and not a subroutine.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 62: Ch. 13: Switching to the C Language
13.3 Interrupts in C
13.3 Interrupts in C

## Slide 63: Ch. 13: Switching to the C Language
13.3 Interrupts in C
13.3 Interrupts in C

## Slide 64: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Using a Port Interrupt on S1 to Toggle LED1 in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_IRQs_Port4_S1
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.

## Slide 65: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Using a Port Interrupt on S1 to Toggle LED1 in C

## Slide 66: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Using a Port Interrupt on S1 to Toggle LED1 in C
Step 3: Save, debug, and run your program.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 67: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.3 Interrupts in C
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 68: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Overflows using ACLK

## Slide 69: Ch. 13: Switching to the C Language
13.4 Timers in C
13.4 Timers in C
Program the timer system:
  Setting up the timer.
  Enabling timer IRQs.
  Creating an ISR that will accomplish the desired task.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 70: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using ACLK in C

## Slide 71: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Toggling LED1 on TB0 Overflow Using ACLK in C

## Slide 72: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using ACLK in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Timers_ACLK_Overflow
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 73: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using ACLK in C
Step 3: Debug your program and run it.

## Slide 74: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Overflows using ACLK
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 75: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Overflows using ACLK & 12-bit Length

## Slide 76: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using ACLK and 12-bit Counter Configuration in C

## Slide 77: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Toggling LED1 on TB0 Overflow Using ACLK (12-bit) in C

## Slide 78: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using ACLK and 12-bit Counter Configuration in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Timers_ACLK_Overflow_12bit
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 79: Ch. 13: Switching to the C Language
13.4 Timers in C
Step 3: Debug your program and run it.
Ex: Toggling LED1 on TB0 Overflow Using ACLK and 12-bit Counter Configuration in C

## Slide 80: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Overflows using ACLK & 12-bit Length
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 81: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Overflows using SMCLK

## Slide 82: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using SMCLK in C

## Slide 83: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Toggling LED1 on TB0 Overflow Using SMCLK in C

## Slide 84: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using SMCLK in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Timers_SMCLK_Overflow
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 85: Ch. 13: Switching to the C Language
13.4 Timers in C
Step 3: Debug your program and run it.
Ex: Toggling LED1 on TB0 Overflow Using SMCLK in C

## Slide 86: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Overflows using SMCLK
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 87: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Overflows using SMCLK & a Divide-by-4 Pre-Scalar

## Slide 88: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using SMCLK and a Divide-by-4 Clock Configuration in C

## Slide 89: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Toggling LED1 on TB0 Overflow Using SMCLK and a Divide-by-4 Clock Configuration in C

## Slide 90: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 on TB0 Overflow Using SMCLK and a Divide-by-4 Clock Configuration in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Timers_SMCLK_Overflow_Div4
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 91: Ch. 13: Switching to the C Language
13.4 Timers in C
Step 3: Debug your program and run it.
Ex: Toggling LED1 on TB0 Overflow Using SMCLK and a Divide-by-4 Clock Configuration in C

## Slide 92: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Overflows using SMCLK & a Divide-by-4 Pre-Scalar
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 93: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Compares using CCR0

## Slide 94: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Compares using CCR0

## Slide 95: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 Using a CCR0 Compare in C

## Slide 96: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Toggling LED1 Using a CCR0 Compare in C

## Slide 97: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Toggling LED1 Using a CCR0 Compare in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Timers_Compare_CCR0
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 98: Ch. 13: Switching to the C Language
13.4 Timers in C
Step 3: Debug your program and run it.
Ex: Toggling LED1 Using a CCR0 Compare in C

## Slide 99: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Timer Compares using CCR0
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 100: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Generating PWMs with Timer Compares

## Slide 101: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Flashing LED1 with a 5% Duty Cycle PWM Using Multiple Compares in C

## Slide 102: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Flashing LED1 with a 5% Duty Cycle PWM Using Multiple Compares in C

## Slide 103: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex: Flashing LED1 with a 5% Duty Cycle PWM Using Multiple Compares in C
Period
Duty Cycle

## Slide 104: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Flashing LED1 with a 5% Duty Cycle PWM Using Multiple Compares in C
Step 1: Create a new C/C++ Empty Project (with main.c) titled:
C_Timers_Compare_CCR1_n_CCR0_PWM
Step 2: Type in the following code into the main.c file after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 105: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Flashing LED1 with a 5% Duty Cycle PWM Using Multiple Compares in C

## Slide 106: Ch. 13: Switching to the C Language
13.4 Timers in C
Ex: Flashing LED1 with a 5% Duty Cycle PWM Using Multiple Compares in C
Step 3: Debug your program and run it. You will see LED1 flash briefly every 1 second.

## Slide 107: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timers in C – Example: Generating PWMs with Timer Compares
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 108: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timer Captures on the MSP430FR2355

## Slide 109: Ch. 13: Switching to the C Language
12.5 Timer Captures on the MSP430FR2355
Timer Captures on the MSP430FR2355

## Slide 110: Ch. 13: Switching to the C Language
12.5 Timer Captures on the MSP430FR2355
Timer Captures on the MSP430FR2355

## Slide 111: Ch. 13: Switching to the C Language
12.5 Timer Captures on the MSP430FR2355
Ex. Timer Captures on the MSP430FR2355 (SW trig)

## Slide 112: Ch. 13: Switching to the C Language
13.3 Interrupts in C
Ex. Timer Captures on the MSP430FR2355 (SW trig)

## Slide 113: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 13: Switching to the C Language
13.4 Timer Captures on the MSP430FR2355
www.youtube.com/c/DigitalLogicProgramming_LaMeres